## Slide 1: BE Project 2012 on
Fr. Conceicao Rodrigues College of Engineering
Ashish Belokar
Kshitij Dholakia
Swapnil Kate
Localization and Mapping with a Mobile Robot and Kinect sensor

## Slide 2: Problem Statement
To develop a Mobile Robot
  Localization
    Pose estimates: (x, y, theta)
  Mapping
    Register observations

## Slide 6: Robot Description
Drive
Motors
Motor Driver
Encoders
Batteries
Microcontroller
Kinect sensor

## Slide 7: Kinect sensor
RGB from VGA camera
Depth/Distance values from IR sensor
Result = Point Cloud

## Slide 9: Software Requirements
Operating System
  Ubuntu 11.10
  Robot Operating System
Programming
  C++
Drivers
  OpenNI for Kinect

## Slide 10: Robot Operating System
Hardware abstraction
Low-level device control
Process Management
Message Passing System
  Synchronous
  Asynchronous

## Slide 11: ROS Concepts
File System:
  Packages and Stacks
Computational Graph:
  Nodes (Publisher and/or Subscriber)
  Topics
  Messages

## Slide 12: ROS Architecture

## Slide 13: Kinematic analysis
30 slots in the wheel encoder
30 interrupts/counts ≡ 2*PI*R centimeters
Therefore, distance in cm for count value “x”:
  = (2*PI*R*x)/30
  Distance travelled D =
  (Left motor (Dl) + Right motor (Dr))/2

## Slide 14: Kinematic analysis
Dl
Dr
=

## Slide 15: Kinematic analysis
(Dl - Dr)
b

## Slide 16: Kinematic analysis
(Dl - Dr)
b
Theta = (Dl - Dr)/b

## Slide 17: Kinematic analysis
(Dl - Dr)
b
Theta = (Dl - Dr)/b
X = D*cos(theta)
Y = D*sin(theta)

## Slide 18: Coordinate Frame Transforms

## Slide 19: Modeling it into ROS
Using ROS Message type:
  geometry_msgs/PoseStamped
    Timestamp
    x, y, theta
Using /tf ROS package

## Slide 20: Gmapping
Depth Map to Laser Scan
Odometry values
/tf
P((x, y, theta), map | control_signal, scan_observation)

## Slide 21: Future Work
Output is a 2D Occupancy Grid
Navigation
Path planning
Kinect -> Point clouds
  3D Occupancy grid
  Trajectory planning for robot manipulators